## Slide 1: Exploring PWM Subsystem and its usage in Embedded Devices
M Tamseel Shams

## Slide 2: Agenda
Introduction to PWM
PWM Subsystem in Kernel
PWM Driver implementation
Generic PWM Framework
Legacy PWM Driver (based on Samsung PWM Driver)
Using PWM Subsystem with Sysfs interface
Use-cases of PWM

## Slide 3: Introduction to PWM
Pulse Width Modulator
Method for changing how long square wave stays “ON”
A technique for delivering partial power to a load via digital means
Operates like a switch – continuous ON and OFF
Keywords:
  Duty Cycle
  Modulating Frequency
Figure Link: https://i.stack.imgur.com/3vesi.png

## Slide 4: Introduction to PWM
Period (T)
VL
VH
On
Off
Figure Link: https://cdn.sparkfun.com/assets/f/9/c/8/a/512e869bce395fbc64000002.JPG
https://raw.githubusercontent.com/OnionIoT/Onion-Docs/master/Omega2/Kit-Guides/img/pwm-signals.jpg

## Slide 5: Introduction to PWM
Use-Cases
Figure Link: https://upload.wikimedia.org/wikipedia/commons/thumb/c/cb/RBG-LED.jpg/250px-RBG-LED.jpg
https://upload.wikimedia.org/wikipedia/commons/thumb/4/40/Erdfunkstelle_Raisting_2.jpg/220px-Erdfunkstelle_Raisting_2.jpg
https://m.media-amazon.com/images/I/51cLoRKUcsL._SL1080_.jpg

## Slide 6: PWM Subsystem in Kernel
Two types of APIs
  In-Kernel APIs (or PWM Kernel drivers)
    drivers/pwm/core.c, drivers/pwm/pwm-samsung.c, etc.
  user-space API in /sys/class/pwm
    drivers/pwm/sysfs.c
Identifying PWMs
  Legacy PWM driver files uses unique ID to refer PWM device
  Nowadays, driver file contain static mapping that can be used to match PWM consumers and providers

## Slide 7: PWM Driver Implementation
Two ways to implement PWM driver:
  Board/Consumer specific API – own pwm_*() functions
    e.g. – pwm_samsung_request(), pwm_samsung_config(), etc.
  Generic PWM Framework
    e.g. – pwm_request(), pwm_config(), etc.
    pwmchip_add() – to add a new PWM controller/chip
    pwmchip_remove() – to remove
    struct pwm_chip provides description of PWM chip

## Slide 8: Generic PWM Framework
To provide flexibility – Generic PWM APIs
Why Generic PWM Framework? (Locking Issue)
  pwm_request() and pwm_free() are protected by mutex
  pwm_enable(), pwm_disable() and pwm_config() do not use locking
  Issue from previous barebone API (Board/consumer specific)

## Slide 9: Generic PWM Framework
Request of PWM device
  pwm_request() – (Deprecated now)
  pwm_get() – via lookup
  of_pwm_get() – via PWM framework (using “pwms” property)
Free PWM device
  pwm_free() – (Deprecated now)
  pwm_put()
Managed variants of pwm_get():
  devm_pwm_get() - resource managed pwm_get()
  devm_of_pwm_get() – resource managed of_pwm_get()
  devm_fwnode_pwm_get() – resource managed PWM from firmware node

## Slide 10: Generic PWM Framework
Structure for PWM Channel
hwpwm

## Slide 11: Generic PWM Framework
Structure for PWM Chip/Controller
npwm
0, 1, 2, 3 represents “base”

## Slide 12: Generic PWM Framework
Configuration of PWM – pwm_apply_state()
  Controls PWM period and duty cycle
  Controls enable and disable state
  Controls usage power setting
pwm_config(), pwm_enable() and pwm_disable() – individual substitutes for pwm_apply_state()
pwm_get_state() – gives the present PWM state

## Slide 13: Generic PWM Framework
PWM APIs also exposes PWM arguments
  reference PWM config to be used
  helps in reconfiguration during resume
PWM arguments retrieved using pwm_get_args()
struct pwm_args – 2 fields (period and polarity)
  Used for initial PWM config (usually during probe)

## Slide 14: Legacy PWM Driver Implementation
Based on Samsung PWM Driver
  drivers/pwm/pwm-samsung.c
PWM Arguments
  struct samsung_pwm_channel – Data of PWM channels
  struct samsung_pwm_chip – Data of PWM chip

## Slide 15: Legacy PWM Driver Implementation
Probe, remove and PM
  pwm_samsung_probe()
  pwm_samsung_remove()
  pwm_samsung_resume()
Request and Free
  pwm_samsung_request()
  pwm_samsung_free()
pwm_samsung_config()
  Configures PWM, sets duty cycle and period, updates PWM
  registers

## Slide 16: Legacy PWM Driver Implementation
pwm_samsung_enable() – Enables/starts PWM
pwm_samsung_disable() – Disables/stops PWM
There are few wrapper functions:
  pwm_samsung_set_polarity()
  pwm_samsung_manual_update()

## Slide 17: PWM Driver Implementation
Relation between platform specific PWM structure and Generic PWM structure

## Slide 18: Using PWM Subsystem with sysfs interface
CONFIG_SYSFS needs to be enabled
Exposed at /sys/class/pwm
Probed PWM chips/controllers exported as pwmchipN
  /sys/class/pwm/pwmchip0/
  /sys/class/pwm/pwmchip1/
  and so on…
Inside this directory
  npwm – No. of PWM channel supported
  export – exports a PWM channel for sysfs use
  unexport – unexports a PWM channel from sysfs

## Slide 19: Using PWM Subsystem with sysfs interface
On exporting PWM channel, a pwmX directory is created (0<=x<=npwm-1)
Properties inside this directory:
  period – total period of PWM signal
  duty_cycle – Active time of PWM signal
  polarity – polarity of PWM signal (“normal” or “inversed”)
  enable – enables(1) or disables(0) PWM signal
  capture – details about PWM configuration

## Slide 20: Using PWM Subsystem with sysfs interface
Usage commands:
  Display number of channels supported
    cat /sys/class/pwm/pwmchip0/npwm
  Export PWM Chip
    echo 0 > /sys/class/pwm/pwmchip0/export
  Set Period and Duty Cycle
    echo 1000000 > /sys/class/pwm/pwmchip0/pwm0/period
    echo 500000 > /sys/class/pwm/pwmchip0/pwm0/duty_cycle

## Slide 21: Using PWM Subsystem with sysfs interface
Usage commands:
  Set Polarity
    echo “normal” > /sys/class/pwm/pwmchip0/pwm0/polarity
    echo “inversed” > /sys/class/pwm/pwmchip0/pwm0/polarity
  Enable PWM timer
    echo 1 > /sys/class/pwm/pwmchip0/pwm0/enable
  Disable PWM timer
    echo 0 > /sys/class/pwm/pwmchip0/pwm0/enable
  Unexport PWM chip
    echo 0 > /sys/class/pwm/pwmchip0/unexport

## Slide 22: Use-Cases of PWM
CPU and GPU
  PWM fans are used in CPU coolers and GPU (graphic card) coolers
  Use an integrated circuit to control speed of fan
  Control how much cooling is provided to CPU and GPU
Figure Link: https://www.aliexpress.com/item/4000796247648.html

## Slide 23: Use-Cases of PWM
Brightness of Bulb/LEDs
  PWM is a very common method of dimming LED and Bulb lights
  It works by very rapidly turning them on and off (pulsing), that visually appear as a steady dimmed light
  We adjust the brightness level by adjusting the percentage of the time the lights are on (100% duty cycle) to the time they are off (0% duty cycle)
Figure Link: https://www.pcboard.ca/image/cache/catalog/products/led_drivers/standup-driver/pwm-driver-connection-800x800.jpg

## Slide 24: Use-Cases of PWM
Switches
  Used in control circuit to control ON and OFF of switches
  e.g. – used in controlling MOSFET

## Slide 25: Use-Cases of PWM
Telecommunications
  Width of pulses corresponding to specific data values encoded at one end and decoded at other.
  Pulses of various lengths (the information itself) will be sent at regular interval (the carrier frequency of the modulation).
Figure Link: https://en.wikipedia.org/wiki/Pulse-width_modulation

## Slide 26: Use-Cases of PWM
Robotics
  PWM signals are used to control the speed of robot by controlling motors
  Motors will in turn control different part of robot
Figure Link: https://cdn.sparkfun.com/assets/8/2/c/8/3/512e85a6ce395f4d64000000.jpg
https://rukminim1.flixcart.com/image/416/416/kpmy8i80/learning-toy/y/v/q/pwm-dc-motor-speed-controller-1000w-15a-sunrobotics-original-imag3tmvg8phqzgb.jpeg?q=70

## Slide 27: Use-Cases of PWM
Audio Effects and Amplification
  Used in music synthesis (especially subtractive synthesis)
  PWM signal is difference of two saw-toothed waves with one of them inverted
  Ratio of high level and low level is modulated with low frequency oscillator
  On varying duty cycle of pulse, we can create timbral variations
  Duty cycle for soundtracks of video games are normally 50%, 25% and 12.5%
Figure Link: https://www.theengineeringknowledge.com/wp-content/uploads/2020/04/class-D-audio-amplifier-300x107.jpg
https://www.adam-audio.com/content/uploads/2016/09/adam-audio-technologies-pwm-amplifier-768x512.jpg

## Slide 28: Use-Cases of PWM
Inverters
  Used in controlling the inverters voltage which is used in many applications like in AC motors and special motors
  Device’s efficiency depends on harmonic content of PWM signal
Figure Link: https://www.electroschematics.com/wp-content/uploads/2010/07/PWM-Inverter-Block-Diagram.png?w=624

## Slide 29: Conclusion
PWM is believed to be discrete device with no fixed purpose
But, nowadays PWM is being used as a important component in useful devices like
  Fan coolers in heavy load CPUs and GPUs
  Inverters
  Transformers
  Switches
  Robotics (in motors), etc
There is a very flexible and well maintained PWM subsystem in Linux Kernel to efficiently use PWM devices

## Slide 30
Any Questions ?